## PART 1: HeartFelt® Baffle Ceiling GENERAL

  - INTRODUCTION

Supply and fix HeartFelt® Baffle Ceiling System as manufactured by Hunter Douglas Architectural.

  - DESCRIPTION OF THE SYSTEM

The system will consist of box-shaped baffles fixed to an adjustable suspension system which allows for individual baffles to be removed by hand. System to feature open spaces between the baffles.

## PART 2: PRODUCT

_________m2 HeartFelt® Baffle Ceiling, featuring open spaces* and consisting of:

*typically the space between the baffles equals the baffle height

  - PANELS

- Baffle 40HB200, size 40x200 mm (wxh)

- Baffle 50HB250, size 50x250 mm (wxh)

- Baffle 80HB400, size 80x400 mm (wxh)

- Baffle xxHBxxx, non-standard sizes from 40x100 mm (wxh) up to 100x500 mm (wxh)

Baffles to be manufactured from 6.5mm thick polyester felt material

Baffles have square sides and upper edge flanges that are folded inwards and inserted into an aluminium holding profile. Baffles to feature the following executions of the ends:

- Open ends

- Closed ends with separate end caps

- Closed ends where the ending is folded from specially shaped material edges*.

- Any combination of the above options*.

*a folded closed end has a limitation on the maximum possible baffle length

Baffles to have a length of _________mm (manufacturer availability 200-2000 mm). Baffles to be coupled in longitudinal direction by means of panel splices.

Baffles provided with spring clips and locking clips (2 pcs per baffles) to hold and secure baffles in modules ranging from 50 up to 500mm. Modules can vary in steps of 50mm.

  - SUSPENSION

Rows of 0.6mm steel roll formed carriers shall be installed at ________centre on centre by means of adjustable suspensions at a distance of_______, center on centre. Carriers will be joined by means of carrier splices.

Rows of 0.6mm steel roll formed stabilisation profiles shall be installed at ________centre on centre on top of the carriers by means of steel stabilisation brackets.    Carriers and stabilisation profiles are standard available in black (1863).

## PART 3: ADDITIONAL SPECIFICATIONS

  - ACOUSTICS

The HeartFelt® Baffles have inherent acoustical properties. Where required, the installer can place additional acoustical pads.

  - COLOURS

Architect will make a colour selection from the standard Hunter Douglas colour range for HeartFelt® Baffles code no.____.

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.